## Slide 1: The PICAN EEG Toolkit
Greg Siegle, Ph.D.
Josh Barback, B.S., M.F.A.
Program in Cognitive Affective Neuroscience (PICAN)

## Slide 2: On analyzing EEG
Load the data
(Electrodes x samples)
Preprocess (mV, rescale outliers, etc) (may be done in BESA)
Decompose into frequencies and extract those you want
(Electrodes x samples)
If EEG
Break the data into trials
(Trials x Electrodes x Samples/Trial)
Average across trials in a condition (Conditions x Electrodes x Samples/Trial)
Extract some parameter e.g., N200
(Conditions x Electrodes)
Group waveform analysis
Group Topology analysis

## Slide 3: The PICAN EEG Toolkit
In
  \\oacres3\rcn\pican\MatlabCode\PupilToolkit\picaneeg
  On Oaclresi: /data/Siegle/matlab/picaneeg
Inherits from and needs to operate:
  the Pupil Toolkit
    \\oacres3\rcn\pican\MatlabCode\PupilToolkit
  EEGlab, an Open Source Matlab Toolbox for Electrophysiological Research
    sccn.ucsd.edu/eeglab/

## Slide 4: Functions for single subject analysis
 | Function | Explanation
Reading data | picaneeg_loadraw | Loads data from any net
 | picaneeg_addnetdata | Adds electrode placement information
 | picaneeg_biosemi_procevents | Extracts events from the biosemi system
Processing data | picaneeg_noisefilter | Filters data – most useful for ERP
 | picaneeg_indivalphafreq | Finds an individually tailored alpha range
 | picaneeg_segmenttrials | Breaks data up into trials
 | picaneeg_dropbadtrials | Rejects trials outside 75 mV
 | picaneeg_condmeans | gets the trial and condition related averages within some time window
 | picaneeg_getmontageavg | gets the condition related averages for certain electrodes
Plotting | picaneeg_plottimeseries | Shows complete time-series for all electrodes, stacked vertically
 | picaneeg_animtopo | Animates a topographic map over time
 | picaneeg_condtopo | show the condition means on a topographic scalp
 | picaneeg_plotcondmeans | shows condition-related means for all conditions for all or just some electrodes
 | picaneeg_plotallcondtrials | shows all trials

## Slide 5: Examples
Single Subject Analyses
  picaneegexample_continuousalpha_emotiv
    continuous alpha from the EMOTIV system
  picaneegexample_N2flanker_biosemi
    N2 from the BIOSEMI system
Group analysis
  picaneegexample_group_continuousalpha_emotiv
    Continuous alpha over many participants – average topomaps

## Slide 6: Biosemi N2 Flanker example
function p=picaneegexample_N2flanker_biosemi(fname,graphics)
% example of working with PICAN eeg functions
% for N2 from a flanker task for the BioSemi system
% usage: p=picaneegexample_alphatrials_emotiv;
if nargin<1, fname='C:\greg\papers\cidar\data\erp\eeg\2265_03flanker.bdf'; end
if nargin<2, graphics=1; end
minfilterfreq=.01; maxfilterfreq=30; % hz filters for ERP analyses
starttime=100; endtime=300; peaktime=200; % time offsets for N2
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%% Loading the data
p=picanproceeg(fname,0,0); % 0,0 means no frequency data processed
p=picaneegaddnetdata(p); % add electrode placement
p=biosemi_procevents(p); % find event codes
p=picaneegnoisefilter(p,minfilterfreq,maxfilterfreq); % filter from .01 to 30Hz - only for ERP analyses
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%% Design Specific Code - MODIFY THIS
% suppose every 2 seconds represents a new window of interest
p.TrialStarts=p.EventTicks(1:2:end);
p.TrialEnds=[p.TrialStarts(2:end) size(p.OtherData,2)];
p.TrialLengths=[p.TrialEnds-p.TrialStarts];
p.TrialTypes=p.EventCodes(1:2:end);
p.CondLabels={'Congruent','Incongruent'};
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%% Segmenting the data into trials and getting Condition-Related averages and stats
p=picansegmenteegtrials(p); % breaks the data into trials
%pcolor(p.EEGind); shading flat % shows all electrodes
p=picaneegdropbadtrials(p); % drops bad trials
p=picangeteegtimewin(p,starttime,endtime); % gets the trial and condition related averages between 100 and 300ms
p.selectedtrialavg=picangetmontavg(p,[3 12],'Min'); % gets the condition related averages for certain electrodes, here F3 and F4
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%% Plotting functions
if graphics
%figure(1); picanploteegtimeseries(p); % shows time-seriesp.selectedtrialavg=picangetmontavg(p,[3 12],'Mean'); % gets the condition related averages for certain electrodes, here F3 and F4
%figure(2); picananimtopo(p); % animate time series
figure(3); clf; picaneegcondtopo(p); % show the condition means on a topographic scalp
figure(4); clf; picanploteegcondmeans(p); % shows condition-related means for all conditions
% alternately can show just one condition using eeglab native functions
figure(5); clf; plottopo(squeeze(p.CondMeans(1,:,:)),p.chanlocs); % condition 1
figure(6); clf; plottopo(squeeze(p.CondMeans(2,:,:)),p.chanlocs); % condition 2
figure(7); clf; picanploteegcondmeans(p,{'Fz','Cz','Pz','Oz'});
condnum=0; sorttime=peaktime; % sorttime in ms
figure(8); clf; picaneegplotallcondtrials(p,'Fz',condnum,sorttime);
end
%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%%
%% writing output
picanwriteeegstats(p,'Min');

## Slide 7: Loading data: picaneeg_loadraw - Loads data from any net - minimal outlier rescaling - conversion to frequency domain if requested
p =
fname: 'Heaven Day 1 Trial 01.edf'
SampleRate: 128
ChanLabels: {14x1 cell}
EEGind: [14x4608 double]
freqlb: 8
frequb: 12
OtherData: [2x4608 double]
netname: 'emotiv_edf'
p=picaneeg_loadraw(fname,8,12);
function p=picaneeg_loadraw(fname,freqlb,frequb,enet,makesmall, absorrel,graphics,dorescaleoutliers)
% freqlb and frequb are the frequency band to examine with wavelet power
% note - this is NOT a band-pass filter. Rather, a running power
% estimate is returned
% for ERP use freqlb=0, frequb=0
% enet is one of:
% biosemi_bdf
% besa_dat
% emotiv_edf
% makesmall means save only the data used by pican routines
% useful because eeg is so big
% absorrel is one of
% 'abs' - absolute power transformed as log(x)
% 'rel' - relative power transformed as log(x+1)/log(x-1)
% graphics is whether plots are produced
% 1=make plots
% 0=no plots
% dorescaleoutliers
% 1=Windsorize outliers outside Tukey hinges
% 0=don't Windsorize

## Slide 8: Loading data: picaneeg_loadraw - Loads data from any net - minimal outlier rescaling - conversion to frequency domain if requested
p =
fname: '2265_03flanker.bdf'
SampleRate: 512
ChanLabels: {128x1 cell}
EEGind: [128x612352 double]
freqlb: 0
frequb: 0
OtherData: [9x612352 double]
netname: 'biosemi_bdf'
p=picaneeg_loadraw(fname,0,0);
function p=picaneeg_loadraw(fname,freqlb,frequb,enet,makesmall, absorrel,graphics,dorescaleoutliers)
% freqlb and frequb are the frequency band to examine with wavelet power
% note - this is NOT a band-pass filter. Rather, a running power
% estimate is returned
% for ERP use freqlb=0, frequb=0
% enet is one of:
% biosemi_bdf
% besa_dat
% emotiv_edf
% makesmall means save only the data used by pican routines
% useful because eeg is so big
% absorrel is one of
% 'abs' - absolute power transformed as log(x)
% 'rel' - relative power transformed as log(x+1)/log(x-1)
% graphics is whether plots are produced
% 1=make plots
% 0=no plots
% dorescaleoutliers
% 1=Windsorize outliers outside Tukey hinges
% 0=don't Windsorize
Channels x samples

## Slide 9: Loading data: picaneeg_addnetdata Adds electrode placement information
p=picaneeg_addnetdata(p)
fname: ‘2265_03flanker.bdf'
SampleRate: 512
ChanLabels: {128x1 cell}
EEGind: [128x612352 double]
freqlb: 0
frequb: 0
OtherData: [9x612352 double]
netname: 'biosemi_bdf'
chanlocs: [1x128 struct]
>> p.chanlocs(1)
ans =
theta: -39.9930
radius: 0.6107
labels: 'A1'
sph_theta: 39.9930
sph_phi: -19.9206
sph_theta_besa: -109.9206
sph_phi_besa: -50.0070
X: 0.7203
Y: 0.6042
Z: -0.3407

## Slide 10: Loading data: picaneeg_biosemi_procevents Adds event codes
p=picaneeg_biosemi_procevents(p);
fname: '2265_03flanker.bdf'
SampleRate: 512
ChanLabels: {128x1 cell}
EEGind: [128x612352 double]
freqlb: 0
frequb: 0
OtherData: [9x612352 double]
netname: 'biosemi_bdf'
chanlocs: [1x128 struct]
EventTicks: [1x1200 double]
EventCodes: [1x1200 double]
bar(p.EventTicks(1:200), p.EventCodes(1:200))

## Slide 11: Processing data: picaneeg_noisefilter band-pass filters the data
p=picaneeg_noisefilter(p,.01,30)
fname: '2265_03flanker.bdf'
SampleRate: 512
ChanLabels: {128x1 cell}
EEGind: [128x612352 double]
freqlb: 0
frequb: 0
OtherData: [9x612352 double]
netname: 'biosemi_bdf'
chanlocs: [1x128 struct]
EventTicks: [1x1200 double]
EventCodes: [1x1200 double]
plot(p.EEGind(1,1:1000))
p=picaneeg_noisefilter(p,.01,30)
hold on; plot(p.EEGind(1,1:1000),'r')
legend('unfiltered','filtered')
p=picaneeg_noisefilter(p,minfilterfreq,maxfilterfreq);

## Slide 12: Segmenting data: Adding trial information
p.TrialStarts=p.EventTicks(1:2:end);
p.TrialEnds=[p.TrialStarts(2:end) size(p.OtherData,2)];
p.TrialLengths=[p.TrialEnds-p.TrialStarts];
p.TrialTypes=p.EventCodes(1:2:end);
p.CondLabels={'Congruent','Incongruent'};
fname: 'C:\greg\papers\cidar\data\erp\eeg\2265_03flanker.bdf'
SampleRate: 512
ChanLabels: {128x1 cell}
EEGind: [128x612352 double]
freqlb: 0
frequb: 0
OtherData: [9x612352 double]
netname: 'biosemi_bdf'
chanlocs: [1x128 struct]
EventTicks: [1x1200 double]
EventCodes: [1x1200 double]
TrialStarts: [1x600 double]
TrialEnds: [1x600 double]
TrialLengths: [1x600 double]
TrialTypes: [1x600 double]
CondLabels: {'Congruent' 'Incongruent'}
bar(p.TrialTypes(1:100))
# trials

## Slide 13: Segmenting data: picaneeg_segmenttrials breaks data into trials
p=picaneeg_segmenttrials(p)
fname: 'C:\greg\papers\cidar\data\erp\eeg\2265_03flanker.bdf'
SampleRate: 512
ChanLabels: {128x1 cell}
EEGind: [128x612352 double]
freqlb: 0
frequb: 0
OtherData: [9x612352 double]
netname: 'biosemi_bdf'
chanlocs: [1x128 struct]
EventTicks: [1x1200 double]
EventCodes: [1x1200 double]
TrialStarts: [1x600 double]
TrialEnds: [1x600 double]
TrialLengths: [1x600 double]
TrialTypes: [1x600 double]
CondLabels: {'Congruent' 'Incongruent'}
EEGTrialData: [600x128x507 double]
plot(squeeze(p.EEGTrialData(1:5,1,:))')
Trials x channels x samples/trial

## Slide 14: Segmenting data: picaneeg_dropbadtrials Drops trials outside the Tukey Hinges
p=picaneeg_dropbadtrials(p);
fname: 'C:\greg\papers\cidar\data\erp\eeg\2265_03flanker.bdf'
SampleRate: 512
ChanLabels: {128x1 cell}
EEGind: [128x612352 double]
freqlb: 0
frequb: 0
OtherData: [9x612352 double]
netname: 'biosemi_bdf'
chanlocs: [1x128 struct]
EventTicks: [1x1200 double]
EventCodes: [1x1200 double]
TrialStarts: [1x600 double]
TrialEnds: [1x600 double]
TrialLengths: [1x600 double]
TrialTypes: [1x600 double]
CondLabels: {'Congruent' 'Incongruent'}
EEGTrialData: [600x128x507 double]
dropcutoff: 125.4937
dropmatrix: [600x128 logical]
Bad channel
Trials x channels

## Slide 15: Averaging data: picaneeg_condmeans gets condition-means and condition- and trial-related stats
p=picaneeg_condmeans(p,100,300)
fname: 'C:\greg\papers\cidar\data\erp\eeg\2265_03flanker.bdf'
SampleRate: 512
ChanLabels: {128x1 cell}
EEGind: [128x612352 double]
freqlb: 0
frequb: 0
OtherData: [9x612352 double]
netname: 'biosemi_bdf'
chanlocs: [1x128 struct]
EventTicks: [1x1200 double]
EventCodes: [1x1200 double]
TrialStarts: [1x600 double]
TrialEnds: [1x600 double]
TrialLengths: [1x600 double]
TrialTypes: [1x600 double]
CondLabels: {'Congruent' 'Incongruent'}
EEGTrialData: [600x128x507 double]
dropcutoff: 125.4937
dropmatrix: [600x128 logical]
winstart: 100
winend: 300
TrialStats: [1x1 struct]
CondMeans: [2x128x507 double]
CondStats: [1x1 struct]
p=picaneeg_condmeans(p,winstart,winend)
plot(squeeze(p.CondMeans(:,1,:))')
conds x channels x samples
>> p.CondStats
ans =
CondMean: [2x128 double]
CondMax: [2x128 double]
CondMin: [2x128 double]
Conds x channels

## Slide 16: Plotting data: picaneeg_condtopo plots topography of condition-related stats
picaneeg_condtopo(p,’Min’);
picaneeg_condtopo(p,'Mean');
Note – must redo Biosemi electrode placement…
picaneeg_condtopo(p,'Mean',1);

## Slide 17: Plotting data: picaneeg_condtopo plots topography of condition-related stats
picaneeg_condtopo(p,'Mean');
Electrode placement is correct for the Emotive system
Note: From
p=picaneegexample_continuousalpha_emotiv

## Slide 18: Plotting data: plottopo plots topography of condition-related waveforms
Note – must redo Biosemi electrode placement…
plottopo(squeeze(p.CondMeans(1,:,:)),p.chanlocs);
Note: Negative plotted up

## Slide 19: Plotting data: picaneeg_plotcondmeans plots condition-related waveforms
picaneeg_plotcondmeans(p,{'Fz','Cz','Pz','Oz'});
N2
N2
picaneeg_plotcondmeans(p, chanlist);
If chanlist is not specified all channels are plotted…
Note: negative plotted up for ERP

## Slide 20: Plotting data: picaneeg_plotallcondtrials plots all trials in a condition sorted by values at some time point
picaneeg_plotallcondtrials(p,'Fz',0,200);
picaneeg_plotallcondtrials(p, channame,condnum,sorttime)
% if condnum is 0, the mean of all conditions is plotted.
% otherwise trials in only one of the conditions is plotted
% sorttime is in ms
The only function where positive is plotted up

## Slide 21: Group Analysis
Group analysis means aggregating either parameters or waveforms
To aggregate parameters, you can
  save them out to a text file and analyze them elsewhere, e.g., SPSS
  Analyze whole scalps accounting for spatial multiple comparisons
To aggregate waveforms
  But must account for spatial as well as temporal multiple comparisons

## Slide 22: Group Topological Analysis: picaneeg_writestats writes statistics per participant for analysis off-line, e.g., in SPSS
picaneeg_writestats(p,’Mean’)
>> p.CondStats
ans =
CondMean: [2x128 double]
CondMax: [2x128 double]
CondMin: [2x128 double]
Conds x channels
Writes a text file with 1 value per channel
6ft7ft Day 4 Trial 01_EEGStats_Mean_9-13Hz_4-3500ms.txt
fname AF3_Alpha F7_Alpha F3_Alpha FC5_Alpha T7_Alpha P7_Alpha O1_Alpha O2_Alpha P8_Alpha T8_Alpha FC6_Alpha F4_Alpha F8_Alpha AF4_Alpha
6ft7ft Day 4 Trial 01.edf 2606.1100 4070.1027 1867.2047 2281.4342 1274.5297 1211.2688 1660.8302 1894.0319 1219.4233 1709.9656 2964.3286 2450.2248 5160.7156 2456.1600

## Slide 23: Group Topological Analysis: picaneeg_groupdiff plots group differences in topology
picaneeg_groupdiff(pall);
pall =
GroupLabels: {'Music' 'No Music'}
SampleRate: 128
ChanLabels: {14x1 cell}
chanlocs: [1x14 struct]
netname: 'emotiv_edf'
winstart: 4
winend: 3500
EEGsummary: [40x14 double]
EEG: [4-D double]
group: [1x40 double]
EEGsummary_grpdiff_t: [1x14 double]
EEGsummary_grpdiff_p: [1x14 double]
pall = picaneeg_
example_
group_
continuousalpha_
emotiv
picaneeg_groupdiff(pall,1); % the 1 says put it on a head
Yes, you can rotate it….
pall=picaneeg_groupdiff(pall,doaspaired,showhead,winstart,winend)
Notes: pall = picaneeg_example_group_continuousalpha_emotiv

## Slide 24: But how do we control type I error across electrodes?
A priori
  Identification of electrodes of interest
To claim localization:
  Cluster thresholding as in fMRI
To not care about localization:
  # electrodes necessary for you to say the groups are different

## Slide 25: Comparing waveforms
Comparing waveforms is not trivial
We have implemented functions for computing tests at every sample along the waveform.
Unless these comparisons are a-priori I recommend using these only in the context of a group x time or condition x time interaction done on a dimension-reduced dataset.
Controlling type I error
  Guthrie & Buchwald’s (1991) technique
    Guthrie D, Buchwald JS (1991): Significance testing of difference potentials. Psychophysiology 28:240-244.
  Blair & Karniski’s (1993) technique
    Blair RC, Karniski W (1993): An alternative method for significance testing of waveform difference potentials. Psychophysiology 30:518-524
The Pupil Toolkit

## Slide 26: T-tests at every sample, marking intervals significantly long enough to care about via Guthrie & Buchwald (1991)
seconds
Never Depressed (41)
Unmedicated Depressed (47)
Regions of significant differences. Yellow is p<threshold you pass as an argument (p<0.1 by default) and red is less than p<.05. The black line is intervals longer than the patch length you pass in.
5
10
15
20
25
0
0.1
0.2
0.3
mm
What’s the emotion?
UGLY
The Pupil Toolkit

## Slide 27: Group Waveform Analysis: picaneeg_groupdiffwaveform plots condition-related waveforms with group differences highlighted
picaneeg_groupdiffwaveform(pall,{'F3','F4','T7','T8'})
Note: Can use regions of significant differences to remake topographic plots, e.g.,
picaneeg_groupdiff(pall,0,0,300,1000)
Ngrp1=20, Ngrp2=20
0.05 to 0.45s: t(38)=-3.67, p=0.00, D=-1314.87, d=-1.16
0.70 to 0.90s: t(38)=-2.35, p=0.02, D=-1364.89, d=-0.74
1.11 to 2.08s: t(38)=-3.52, p=0.00, D=-1876.14, d=-1.11
3.00 to 3.13s: t(38)=-2.06, p=0.05, D=-2218.12, d=-0.65
16.07 to 16.31s: t(38)=-2.01, p=0.05, D=-2358.83, d=-0.64
19.45 to 19.78s: t(38)=-2.35, p=0.02, D=-2033.34, d=-0.74
19.83 to 20.05s: t(38)=-2.24, p=0.03, D=-1734.89, d=-0.71
25.10 to 25.26s: t(38)=-2.39, p=0.02, D=-1647.15, d=-0.76
32.70 to 32.84s: t(38)=-2.11, p=0.04, D=-1803.47, d=-0.67
Stats too…